## Slide 1
Applied Digital Logic Design
(EC1002-2)
Department of E&CE
N.M.A.M. Institute of Technology, Nitte

## Slide 2
Outline
02
Syllabus
Number Systems
Basic and Universal gates
Boolean algebra
Introduction to Combinational Logic
Difference between Analog and Digital Signals

## Slide 3
Syllabus
03

## Slide 4
Syllabus
4
UNIT – I
Fundamentals of Digital Design: Difference between Analog and Digital Signals, Number Systems: Decimal, Binary, Octal and Hexadecimal. Binary Addition and Subtraction, Digital Logic Gates, Boolean Algebra, Boolean Functions: Canonical Forms, Completely and Incompletely Specified Functions, Simplification of Boolean Functions using Boolean Algebra, Karnaugh Map and Quine-McCluskey Method, Realization of Boolean functions using Basic Gates and Universal Gates. 10Hrs

## Slide 5
5
UNIT – II
Combinational Logic and Sequential Logic Circuits: Introduction to Combinational Logic Circuits, Half/Full Adders/Subtractors, Parallel Adders/Subtractors, Binary Comparators, Decoders, Encoders, Multiplexers. Basic Bistable Element, SR Flip-Flop, D Flip Flop, JK Flip Flop, T Flip Flop, Master Slave JK Flip Flop, Characteristic Equations, Conversion of Flip Flops.
10Hrs

## Slide 6
Syllabus
6
UNIT – III
Applications of Flip Flops: Design of Shift Register using D- flip flop, Design of Counters: Asynchronous counters using T-flip flop, Synchronous Counters using D-flip flop and T Flip Flop 5Hrs

## Slide 7
Course Outcomes
7
CO1 Compare Analog and Digital Signals; Convert the number from one numbering system to another;
CO2 Simplify the logic expressions using Boolean Algebra or K-Map or QM Method; Realize the logic expression using Basic/Universal Gates;
CO3 Analyze and Design different Combinational logic circuits such as Decoders, Encoders, Multiplexers, Adders, Subtractors, Binary Comparators
CO4 Describe the operation of Latches, Flip flops, Mater-Slave Flip flops, Edge triggered Flip-flops.
CO5 Make use of Flip flops to design Registers, Synchronous/Asynchronous Counters.

## Slide 8
Text Books
8
T1 Morris Mano, "Digital Design", Prentice Hall of India, Third Edition.
T2 Donald D. Givone, “Digital Principles and Design”, Tata McGraw Hill, 2002.

## Slide 9
Reference Books
9
R1 John M Yarbrough, "Digital Logic Applications and Design", Thomson Learning,
2001.
R2 D. P. Kothari and J. S Dhillon, "Digital Circuits and Design’, Pearson, 2016.
R3 Charles H Roth, "Fundamentals of Logic Design", Cengage Learning.

## Slide 10
NPTEL/ MOOC Links
10
https://nptel.ac.in/courses/117106086

## Slide 11
Evaluation Criteria
11
Assessment Weightage in Marks(Theory) | 
Mid Semester Exam 1 (MSE1) | 20
Mid Semester Exam 2 (MSE2) | 20
Tasks (4+4+2) | 10
Total | 50
60% weightage, converted to 30 Marks, passing Marks :12 | 

## Slide 12
Evaluation Criteria
12
Assessment Weightage in Marks(Practical) | 
Record | 10
Task/Performance | 10
MSE | 30
Total | 50
40% weightage, converted to 20 Marks, passing Marks :8 | 100

## Slide 13
Unit 1 Fundamentals of Digital Design

## Slide 14: Digital and Analog Basic Concepts: Analog Signals
Amplitude
(peak-to-peak)
Amplitude
(peak)
Period
(T)
T
F  1 Hz
Amplitude
Distance above reference line
Cycle
One complete wave
Frequency
Cycles per second .Hertz is the unit used for expressing
frequency. Frequency:
14

## Slide 15: Example of Analog Signals
An analog signal can be any time-varying signal.
Minimum and maximum values can be either positive or negative.
They can be periodic (repeating) or non-periodic.
Sine waves and square waves are two common analog signals.
Note that this square wave is not a digital signal because its minimum value is negative.
0 volts
Sine Wave
Square Wave
(not digital)
Random-Periodic
3

## Slide 16: Digital and Analog Basic Concepts: Digital Signals
Amplitude:
For digital signals, this will ALWAYS be 5volts.
Period:
The time it takes for a periodic signal to repeat. (seconds)
Frequency:
A measure of the number of occurrences of the signal per second. (Hertz, Hz)
Time High (tH):
The time the signal is at 5 v.
Time Low (tL):
The time the signal is at 0 v.
Duty Cycle:
The ratio of tH to the total period (T).
Rising Edge:
A 0-to-1 transition of the signal.
Falling Edge:
A 1-to-0 transition of the signal.
Amplitude
T
F  1 Hz
Frequency:
T
DutyCycle  tH 100%
Period (T)
16

## Slide 17: Example of Digital Signals
Digital signal are commonly referred to as square waves or clock signals.
Their minimum value must be 0 volts, and their maximum
value must be 5 volts.
They can be periodic (repeating) or non-periodic.
The time the signal is high (tH) can vary anywhere from 1% of the period to 99% of the period.
5 volts
0 volts
17

## Slide 18: Differences of Analog and Digital Signals
Analog Signals Digital Signals
Continuous both time and amplitude
Infinite range of values
More exact values, but
more difficult to work with
Storing requires memory
such a signal large
amount of
Processing requires large processing power or more time
Transmitting requires a
large bandwidth
Discrete in time and quantized in amplitude
Finite range of values
Not as exact as analog, but easier to work with
Storing requires memory
such less
a signal amount of
Processing requires low
less
processing power or time
Transmitting requires a less bandwidth than analog
6

## Slide 19: Number Systems
A number system defines how a number can be represented using distinct symbols.
The number the numeral represents is called its value.
A number can be represented differently in different systems
For example, the two numbers (2A)16 and (52)8 both refer to the same quantity, (42)10, but their representations are different
19

## Slide 20: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10(D) | 0, 1, … 9 | Yes | No
Binary | 2(B) | 0, 1 | No | Yes
Octal | 8(O) | 0, 1, … 7 | No | No
Hexa- decimal | 16(H) | 0, 1, … 9, A, B, … F | No | No
Four number system
Decimal (10) , Binary (2), Octal (8) and Hexadecimal(16)
20

## Slide 21: Decimal numbers
In the decimal number systems each of the ten digits, 0 through 9,
represents a certain quantity also known as base-10 number systems
The position of each digit in a decimal number indicates the magnitude of the quantity represented and can be assigned a weight. The weights for whole numbers are positive powers of ten that increases from right to left, beginning with 10º = 1
For fractional numbers, the weights are negative powers of ten that decrease from left to right beginning with 10−1.
21

## Slide 22: Decimal numbers
10^1
10^0
1
10^-1 10^-2 10^-3
0.1 0.01 0.001
Base
10^4 10^3 10^2
10000 1000 100 10
Right of decimal point
left of the decimal point
10

## Slide 23: Decimal numbers
Example: the value 725.194 is represented in expansion form as follows:
7 * 10^2 + 2 * 10^1 + 5 * 10^0 + 1 * 10^-1 + 9 * 10^-2 + 4 * 10^-3
= 7 * 100 + 2 * 10 + 5 * 1 + 1 * 0.1 + 9 * 0.01 + 4 * 0.001
= 700 + 20 + 5 + 0.1 + 0.09 + 0.004
= 725.194
11

## Slide 24: Binary Numbers
Most modern computer system using binary logic. The computer represents values(0,1) using two voltage levels (usually 0V for logic 0 and either +3.3 V or +5V for logic 1).
The Binary Number System uses base 2 includes only the digits 0 and 1 . The position of a 1 or 0 in a binary number indicates its weight, or value within the number, just as the position of a decimal digit determines the value of that digit.
With 4 digits position we can count from zero to 15. In general, with n bits we can count up to a number equal to 2ⁿ - 1.
Largest decimal number = 2𝑛- 1
12

## Slide 25: Binary Numbers
A binary number is a weighted number. The right-most bit is the least significant bit (LSB) in a binary whole number and has a weight of 2º =1. The weights increases from right to left by a power of two for each bit. The left-most bit is the most significant bit (MSB); its weight depends on the size of the binary number.
2^-1
2^-2
32
The weighted values for each position are :
2^5 2^4 2^3 2^2 2^1 2^0
16 8 4 2 1
0.5 0.25
Base
Right of radix point
left of the radix point
13

## Slide 26: Octal Systems
Computer scientists are often looking for shortcuts to do things
One of the ways in which we can represent binary numbers is to use their octal equivalents instead
This is especially helpful when we have to do fairly complicated tasks using numbers
The octal system is composed of eight digits, Known as base-8 number systems which are: 0, 1, 2, 3, 4, 5, 6, 7
To count above 7, begin another column and start over: 10, 11, 12, 13, 14, 15, 16, 17, 20, 21 and so on.
Counting in octal is similar to counting in decimal, except
that the digits 8 and 9 are not used.
14

## Slide 27: Hexadecimal Numbers
The hexadecimal number system has sixteen digits and is used primarily as a compact way of displaying or writing binary numbers because it is very easy to convert between binary and hexadecimal.
Long binary numbers are difficult to read and write because it is easy to drop or transpose a bit. Hexadecimal is widely used in computer and microprocessor applications.
The hexadecimal system known as base-16 number systems,
It is composed of 16 digits and alphabetic characters, which are: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
To count above 16, begin another column and start over:
10, 11, 12, 13, 14…. 1D, 1E, 1F, 20, 21 and so on
The maximum 3-digits hexadecimal number is FFF or decimal 4095 and maximum 4-digit hexadecimal number is FFFF or decimal 65,535

## Slide 28: Number Representation in different systems
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
Quantities/Counting (1 of 3)

## Slide 29: Number Representation in different systems
Quantities/Counting (2 of 3)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 30: Number Representation in different systems
Quantities/Counting (3 of 3)
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
Etc.

## Slide 31: Number System Conversions
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 32: Quick Example
2510 = 110012 = 318 = 1916
Base

## Slide 33: Decimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 34: Decimal to decimal
12510 => 5 x 100 = 5
2 x 101 = 20
1 x 102
= 100
125
Base
Weight

## Slide 35: Fractions
3.14 =>
4 x 10-2
1 x 10-1
3 x 100
= 0.04
= 0.1
= 3
3.14

## Slide 36: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 37: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 38: Example
1010112 | => | 1 | x
 |  | 1 | x
 |  | 0 | x
 |  | 1 | x
 |  | 0 | x
 |  | 1 | x
20
21
22
23
24
25
= | 1
= | 2
= | 0
= | 8
= | 0
= 32
4310
Bit “0”

## Slide 39: Binary to Decimal
1101 = 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20
= 1 x 8 + 1 x 4 + 0 x 2 + 1 x 1
= 8 + 4 + 0 + 1
(1101)2 = (13)10
1, 2, 4, 8, 16, 32, 64, 128, 256, 512, ….

## Slide 40
10.1011 | => | 1 | x
 |  | 1 | x
 |  | 0 | x
 |  | 1 | x
 |  | 0 | x
 |  | 1 | x
= | 0.0625
= | 0.125
= | 0.0
= | 0.5
= | 0.0
= | 2.0
Binary to decimal (Fractions)
2-4
2-3
2-2
2-1
20
21
2.6875

## Slide 41: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 42: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 43: Example
7248 | => | 4 | x
 |  | 2 | x
 |  | 7 | x
80
81
82
= | 4
= | 16
= | 448
 | 46810

## Slide 44: Octal to Decimal
137 = 1 x 82 + 3 x 81 + 7 x 80
= 1 x 64 + 3 x 8 + 7 x 1
= 64 + 24 + 7
(137)8 = (95)10
Digits used in Octal number system – 0 to 7

## Slide 45: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 46: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 47: Example
ABC16 | =>C | x | 160 | = | 12 | x | 1 | = | 12
 | B | x | 161 | = | 11 | x | 16 | = | 176
 | A | x | 162 | = | 10 | x | 256 | = | 2560
274810

## Slide 48: Hex to Decimal
BAD = 11 x 162 + 10 x 161 + 13 x 160
= 11 x 256 + 10 x 16 + 13 x 1
= 2816 + 160 + 13
(BAD)16 = (2989)10
A = 10, B = 11, C = 12, D = 13, E = 14, F = 15

## Slide 49: Number System Conversions
Decimal to Base-k [Successive division]
  Divide the decimal number to be converted by ‘k’
  The remainder from Step 1 is the least significant digit
  Divide the quotient of the previous divide by the ‘k’
  Record the remainder from Step 3 as the next digit
  Repeat Steps 3 and 4, getting remainders from right to left, until the quotient becomes zero in Step 3.
  The last remainder thus obtained will be the Most Significant Digit

## Slide 50: Number System Conversions
Decimal to Base-k [Successive Multiplication]
  Multiply the fractional decimal number, to be converted, by ‘k’
  The integer from Step 1 is the highest order digit
  Multiply the fractional part from Step 1 by the ‘k’
  Record the integer from Step 3 as the next digit
  Repeat Steps 3 and 4, getting integers from left to right, until the fractional part becomes zero in Step 3.

## Slide 51: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 52: Example
12510 = ?2
2 125
2
2
2
2
2
2
62 1
31 0
15 1
7 1
3 1
1 1
0 1
12510 = 11111012

## Slide 53: Decimal to Binary
 | 13
 | 6
 | 3
 | 1
 | 0
2
2
2
2
1
0
1
1
(13)10 = (1101)2
MSB
LSB

## Slide 54: Fractions
Decimal to binary
3.14579
.14579
x 2 0.29158
x 2
0.58316
x 2 1.16632
x 2
0.33264
x 2 0.66528
x 2 1.33056
etc.
11.001001...

## Slide 55: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 56: Example
123410 = ?8
154 2
19 2
2 3
8 1234
8
8
8
0 2
123410 = 23228

## Slide 57: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 58: Example
123410 = ?16
123410 = 4D216
16 1234
16 77 2
16 4 13 = D
0 4

## Slide 59: Decimal to Hex
 | 2989
 | 186
 | 11
 | 0
16
16
16
13
10
11
(2989)10 = (BAD)16
MSP
LSP

## Slide 60: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 61: Binary to Octal
Technique
Binary to Octal [Integers]
  Divide the binary digits into groups of three (starting from the right).
  Convert each group of three binary digits to one octal digit
Binary to Octal [Fractions]
  Divide the binary digits into groups of three (starting from the radix point).
  Convert each group of three binary digits to one octal digit

## Slide 62
Example
10110101112 = ?8
1 | 011 | 010 | 111
1 | 3 | 2 | 7
10110101112 = 13278

## Slide 63: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 64: Binary to Hexadecimal
Technique
Binary to Hexadecimal [Integers]
  Divide the binary digits into groups of four (starting from the right).
  Convert each group of four binary digits to one hexadecimal digit
Binary to Hexadecimal [Fractions]
  Divide the binary digits into groups of four (starting from the radix point).
  Convert each group of four binary digits to one hexadecimal digit

## Slide 65
Example
10101110112 = ?16
10 1011 1011
2 B
B
10101110112 = 2BB16

## Slide 66: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 67: Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 68: Example
10768 = ?16
1 0
7
6
2
3
001 000 111 110
E
10768 = 23E16

## Slide 69: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 70: Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 71: Example
1F0C16 = ?8
1 F
0
C
0001 1111 0000 1100
1
7 4
1F0C16
1
4
= 174148

## Slide 72: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 73: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 74: Example
7058 = ?2
7
0
5
111 000
101
7058 = 1110001012

## Slide 75: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 76: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 77: Example
10AF16 = ?2
1 | 0 | A | F
0001 | 0000 | 1010 | 1111
10AF16 = 00010000101011112

## Slide 78: Decimal to Hex
 | 2989
 | 186
 | 11
 | 0
16
16
16
13
10
11
(2989)10 = (BAD)16
MSP
LSP
(2989.56)10 = (?)16

## Slide 79: Fractions
Decimal to HEX
2989.56
.56
x 16 8.96
x 16
15.36
x 16 5.76
x 16
12.16
x 16 2.56
x 16 8.96
etc.
BAD.8F5C28

## Slide 80: LOGIC GATES
A logic gate is an elementary building block of a digital circuit.
Logic gates can be created using transistor technology, that perform Boolean operations on high (5V) and low(0V) signals.
There are seven logic gates:
  Basic gates: AND, OR and NOT
  Universal gates: NOR and NAND
  Other gates : XOR and XNOR

## Slide 81: AND GATE
For AND gate, if both the inputs are 1 the output is 1; otherwise, the output is 0.

## Slide 82: OR GATE OR Gate: For OR gate, if both the inputs are 0 the output is 0; otherwise, the output is 1.

## Slide 83: NOT GATE NOT Gate: A NOT gate accepts one input signal (0 or 1) and returns the complementary (opposite) signal as output.

## Slide 84: NAND GATE NAND Gate: For NAND (“NOT of AND”) gate, if both the inputs are 1, the output is 0; otherwise, the output is 1.

## Slide 85
NOR GATE
NOR Gate: The NOR (“NOT of OR”) gate, if both the inputs are 0, the output is 1; otherwise, the output is 0.

## Slide 86: XOR GATE XOR Gate: For XOR gate, if both the inputs are same, the output is 0; otherwise, the output is 1.

## Slide 87: XNOR GATE XNOR Gate: For XNOR gate, if both the inputs are same, the output is 1; otherwise, the output is 0.

## Slide 88: PROPERTIES OF BOOLEAN ALGEBRA

## Slide 89: BASIC RULES OF BOOLEAN ALGEBRA

## Slide 90: A+𝐴B = A.1 + 𝐴 B
Proof For A+𝐴 B = A+B
= A(1+B) + 𝐴 B
= A + AB + 𝐴 B
= A + B (A + 𝐴)

## Slide 91
Proof For (A+B)(A+C) = A+BC
(A+B)(A+C) = A.A + A.C + B.A + B.C
= A + A.C + B.A + BC
= A(1+C)+ BA +BC
= A + BA + BC
= A(1+B) + BC
= A +BC

## Slide 92
DeMorgan’s Theorems
(i)
(ii)

## Slide 93: EXAMPLES
1. Implement the Boolean Expression using basic Gates

## Slide 94: 2. Simplify the boolean expression and realize using basic gates.

## Slide 95: 3. Write the boolean expression for the given logic diagram

## Slide 96: Simplifying Boolean expressions using NAND only and NOR only

## Slide 98
Definition of Combinational Logic
Combinational Logic deals with the techniques of “combining” the basic gates into circuits that performs some desired function.
Examples – Adders, Subtractors, Decoders. Encoders, Multipliers etc
Logic circuits without feedback from output to input.
Logic circuits that contain no memory

## Slide 100
General Logic Design Sequence

## Slide 101
Problem statements to Truth Table

## Slide 111
Design the combinational logic circuit which takes two, 2 bit numbers as its inputs and generates an output to indicate when the sum of the two numbers divisible by 3.

## Slide 112
Design the combinational logic circuit which takes two, 2 bit numbers as its inputs and generates an output to indicate when the sum of the two numbers divisible by 3.
A1 | A2 | B1 | B2 | F | MINTERM
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 0 | 
0 | 0 | 1 | 0 | 0 | ’
0 | 0 | 1 | 1 | 1 | A1’ A2’ B1B2
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 0 | 
0 | 1 | 1 | 0 | 1 | A1’A2B1B2’
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 1 | A1A2’B1’B2
1 | 0 | 1 | 0 | 0 | 
1 | 0 | 1 | 1 | 0 | 
1 | 1 | 0 | 0 | 1 | A1A2B1’B2’
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | A1A2B1B2

## Slide 113
A1’ A2’ B1B2
F= A1’A2B1B2’ + A1A2’B1’B2 +A1A2B1’B2’ + A1A2B1B2

## Slide 114: Combinational Logic Specification
Three ways
  Logic Diagram: Graphical representation
  Truth Table: A list that shows all the output states in tabular form for each possible combination of input variable.
  Boolean Equations: Algebraic expression showing the operation of the logic circuit for each input variable.

## Slide 115: Boolean Equations
Also known as Switching equations
A literal is a Boolean Variable or its complement (a, x’, z)
A product term is a literal or the logical product (AND) of multiple literals (ab, x’y, z’y’)
A sum term is a literal or the logical sum (OR) of multiple literals (a+b, a’+b, x’+y’)
A sum of product (SOP) is the logical OR of multiple product terms (ab+bc’+a’b’)
A product of sum (POS) is the logical AND of multiple sum terms[(a+b’)(a’+b’)(a’+b)]

## Slide 116: Minterms
A minterm is a special product of literals, in which each input variable appears exactly once.
A function with n variables has 2n minterms
Each minterm is true for exactly one combination of inputs
Minterm Is true when… Shorthand
x’y’z’ x=0, y=0, z=0 m0
x’y’z x=0, y=0, z=1 m1
x’yz’ x=0, y=1, z=0 m2
x’yz x=0, y=1, z=1 m3
xy’z’ x=1, y=0, z=0 m4
xy’z x=1, y=0, z=1 m5
xyz’ x=1, y=1, z=0 m6
xyz x=1, y=1, z=1 m7

## Slide 117: Sum of Minterms
Sum of minterms expression can be written from the truth table by picking out the rows of the table where the function output is 1.
f = x’y’z’ + x’y’z + x’yz’ + x’yz + xyz’
= m0 + m1 + m2 + m3 + m6
= m(0,1,2,3,6)
f’ = xy’z’ + xy’z + xyz
= m4 + m5 + m7
= m(4,5,7)
f’ contains all the minterms not in f

## Slide 118: Maxterms
A maxterm is a special sum of literals, in which each input variable appears exactly once.
A function with n variables has 2n maxterms
Each maxterm is false for exactly one combination of inputs
Maxterm Is false when… Shorthand
x + y + z x=0, y=0, z=0 M0
x + y + z’ x=0, y=0, z=1 M1
x + y’ + z x=0, y=1, z=0 M2
x + y’ + z’ x=0, y=1, z=1 M3
x’ + y + z x=1, y=0, z=0 M4
x’ + y + z’ x=1, y=0, z=1 M5
x’ + y’ + z x=1, y=1, z=0 M6
x’ + y’ + z’ x=1, y=1, z=1 M7

## Slide 119: Product of Maxterms
Product of maxterms expression can be by picking out the rows of the table where the function output is 0.
f = (x’ + y + z)(x’ + y + z’)(x’ + y’ + z’)
= M4 M5 M7
= M(4,5,7)
f’ = (x + y + z)(x + y + z’)(x + y’ + z)
(x + y’ + z’)(x’ + y’ + z)
= M0 M1 M2 M3 M6
= M(0,1,2,3,6)
f’ contains all the maxterms not in f

## Slide 120: Relation of Minterm to Maxterm
Any minterm mi is the complement of the corresponding maxterm Mi
Maxterm Shorthand
x + y + z M0
x + y + z’ M1
x + y’ + z M2
x + y’ + z M3
x’ + y + z M4
x’ + y + z’ M5
x’ + y’ + z M6
x’ + y’ + z’ M7
Minterm Shorthand
x’y’z’ m0
x’y’z m1
x’yz’ m2
x’yz m3
xy’z’ m4
xy’z m5
xyz’ m6
xyz m7

## Slide 121: Canonical Forms
A Canonical form of a switching equation is one that contains all of the available input variables.
  Canonical Sum of Products: It is a complete set of Minterms that defines when an output is a logical 1
  Canonical Product of sums: It is a complete set of maxterms that defines when an output is a logical 0
Canonical expressions are not simplified and contains redundancies.
f = x’y’ + x’y + xyz’ is a normal expression
x’y’z’ + x’y’z + x’yz’ + x’yz + xyz’ is the canonical form

## Slide 122: Conversion to Canonical Form
SOP to canonical:
  Identify the missing variable in each AND term
  AND the missing term and its complement with the original AND term
  Expand the term by distribution property
POS to canonical:
  Identify the missing variable in each OR term
  OR the missing term and its complement with the original OR term
  Expand the term by distribution property

## Slide 147: Prime Implicants and Essential Prime Implicants
Minimal Sum = x’z’ + yz

## Slide 148
Minimal Sum = z’

## Slide 149: Find the PI and EPI. Also find the minimal SUM

## Slide 151
Minimal sum obtained

## Slide 159
BCD to Excess-3 Conversion

## Slide 162
W=A+BC+BD=A+B(C+D)
X=B’C+B’D+BC’D’=B’(C+D)+BC’D’
Y=CD+C’D’
Z=D’

## Slide 163
Logic Diagram

## Slide 164: J = f (x,y,z) = ∏ (0,3,4,7)
Show the grouping of Maxterms. Mention Prime Implicates and Essential prime implicates. Also Find the Minimal Product .

## Slide 165
Minimal Product

## Slide 167
Minimal Product

## Slide 168: Quine-McCluskey Tabular Method
simplify the following Boolean function, f(W,X,Y,Z)=∑m(2,6,8,9,10,11,14,15) using Quine-McClukey tabular method.

## Slide 173: End of Unit1